## Slide 1: Verification of Flash Flood Warnings
Brent MacAloney
Meteorologist, Performance Branch
Silver Spring, MD

## Slide 2
Historical Flash Flood Verification
Developing a scheme for storm-based flash flood warnings
  How storm-based warnings are verified
Upcoming changes to verification
  Next-Generation Storm Data Program
On Tap Today….

## Slide 3
Verification data back to 1986
Verifying events from storm data
GPRA metric until FY10
County-based verification
  One report in warned county, regardless of if in polygon verifies warning
Historical Flash Flood Verification

## Slide 4
County-based Verification
unwarned
unwarned
unwarned
unwarned
unwarned

## Slide 5
Developing Storm-based FFW Verification
NWS begins issuing storm-based warnings in October 2007 for SVR, TOR, FFW, and SMW products
Needed way to measure performance since county-based methodology no longer applied.
Team formed to develop new performance metrics
  Met in Boulder in December 2005

## Slide 6
How Storm-based FFWs are Verified
Information used from warning products
  Beginning date / time (VTEC)
  Ending date / time (VTEC)
  Forecast office
  Action Code (NEW or EXT)
  Event Tracking Number (ETN)
  Area from latitude/longitude

## Slide 7
How Storm-based FFWs are Verified
Information used from events
  Beginning date / time
  Ending date / time
  Forecast office
  Area from latitude/longitude points outlining flooded area

## Slide 8
How Storm-based FFWs are Verified
First step: Check if the warning verified
  Did a flash flood event occur within the area and time of the warning?
    Yes, warning is verified.
    No, warning is unverified
UNVERIFIED
VERIFIED

## Slide 9
How Storm-based FFWs are Verified
Second step: Calculate percent of event warned (PEW)
  Was there a flash flood warning valid for the area and time in which the event occurred?
    Yes, event is fully warned, PEW = 1
    Partially, event is partially warned, PEW between 0 - 1
    No, event is unwarned, PEW = 0

## Slide 10
Event fully warned in time and area

## Slide 11
Event partially warned in time and area

## Slide 12
Event partially warned in time and area

## Slide 13
Event not warned in time and/or area

## Slide 14
How Storm-based FFWs are Verified
Third step: Calculate event maximum event lead time
  Was there a flash flood warning valid any area of the event at the time in which the event occurred?
    Yes, lead time > 0
    No, lead time = 0
Note: Maximum event lead time calculation does not take into account how much of event was covered by a warning.

## Slide 15
Event with maximum event lead time > 0
Maximum event lead time = 7 minutes

## Slide 16
Event with maximum event lead time > 0
Maximum event lead time = 119 minutes

## Slide 17
Event with no maximum event lead time
Maximum event lead time = 0 minutes

## Slide 18
How Storm-based FFWs are Verified
Fourth step: Calculate event area weighted lead time
  Was there a flash flood warning valid at the time in which the event occurred?
    Yes
      Did the warning cover the entire area of the event?
        Yes, lead time > 0
        No, deduction taken on lead time for area not warned
    No, lead time = 0

## Slide 19
Event with area weighted lead time > 0
Area weighted lead time = 7 minutes

## Slide 20
Event with area weighted lead time > 0
Area weighted lead time = 69 minutes

## Slide 21
Event with no area weighted lead time
Area weighted lead time = 0 minutes

## Slide 22
Difference between area weighted and maximum event lead times
Area LT = 69 minutes
Max LT = 119 minutes
Which best shows our
performance?

## Slide 23
Verification data back to October 2007
Verifying events from storm data
GPRA metric since FY10
Storm-based Flash Flood Verification

## Slide 24
Storm data currently being modernized
Beginning with data in October 2010
Changes will impact verification of flash floods
Changes to Verification

## Slide 25
Change to how events are entered
Problem – “Events in storm data are broken into county-based segments.

## Slide 26
Change to how events are entered
Solution – Eliminate the need to enter events into county-based events
All county-based events will be able to be entered “as they occurred” and won’t have to be broken up into county-based segments.
Biggest impact to tornado, hail, thunderstorm wind, flash flood and flood

## Slide 27
Change to how events are entered
Benefit of eliminating county-boundaries:
  More accurate reporting of events
  Easier entry into storm data
  Saves a lot of entry time

## Slide 28
Thank you for your time! Feel free to contact me….
Brent MacAloney
E-mail: Brent.MacAloney@noaa.gov
Phone: 301-713-0090 x135