## Slide 1: A Review of the Whittenton Dam Crisis
Nicole M. Belk
Senior Service Hydrologist
NWS Weather Forecast Office, Taunton, MA
David R. Vallee
Hydrologist-in-Charge
NWS Northeast River Forecast Center, Taunton, MA

## Slide 2: Objectives
Review Hydro-meteorological evolution of events leading up to the potential dam failure
Examine the flood potential should the Whittenton Pond and/or Morey’s Bridge Dam had failed
Discuss the WFO/RFC capabilities to provide support during dam failure events

## Slide 3: Hydro-met perspective
Back to back prolific rainfall events
  October 7-9 and October 13-16
First system dropped 3-5 inches
Second system dropped 6-8 inches
Both systems were linked to the deep tropics – deep moisture plume

## Slide 4: Round One: Tropical Storm Tammy remnants and a slow moving frontal system
October 7-9, 2005

## Slide 7
24 Hour Precipitation for October 8th, 2005

## Slide 8
24 Hour Precipitation for October 9th, 2005
SE Massachusetts
Event Total: 3-5”

## Slide 9: Round Two: Off-shore storm development and remnants of Subtropical TD 22
October 13-16, 2005

## Slide 11
24 Hour Precipitation for October 14th, 2005

## Slide 12
24 Hour Precipitation for October 15th, 2005

## Slide 13
24 Hour Precipitation for October 16th, 2005
SE Massachusetts
Event Total: 6-8”
(most of this fell in a 6 to 12 hour period)

## Slide 14: Examining the Potential Dam Failure(s)
Crisis began 3 pm, Monday, Oct 17th
  Taunton EMA called in the imminent failure of Whittenton Dam on the Mill River
    Just upstream of the city center
Two structures at risk:
Most immediate concern: Whittenton Dam
  Built in the late 1800s, limited refurbishment in 1950s
Complicating matters: Morey’s Bridge Dam
  Holding back Lake Sabattia

## Slide 16
Whittenton Pond Dam
Downtown Taunton, MA

## Slide 17: NWS Capabilities What we need from you
Have your local NWS office high on the local notification list for dams in your area
  High Hazard dams have Emergency Action Plans (EAPs) – ensure the NWS is high on the notification tree
Most important information for the dam:
  The correct name of the dam!
  County & town the dam is located
  River, stream or lake the dam is on
  NID or State ID, Dam Type (earth, concrete)
  Condition of the dam
    Width of breach
    Is the failure in progress or imminent
    Is the pool/lake full, ½ full, etc.

## Slide 18: NWS Capabilities What we will provide you
Initial estimate of flood wave and the time to reach the nearest downstream location
  For Whittenton Dam – a Flash Flood Warning was issued almost immediately after notification from EMA
  Time to fail = 5 minutes; a flood wave producing a peak depth of 5 feet reaching downtown Taunton in ~ 20 minutes

## Slide 19: Scenario One: Whittenton Fails
Additional Capabilities If Time Allows!

## Slide 20
City of interest: Taunton
Time elapsed from failure to Peak depth at Taunton: 8-14 minutes
Peak depth of flood: 5.4 feet – flood elevation exceeded for 1 hour

## Slide 21
Additional Capabilities If Time Allows!
Scenario Two: Morey’s Bridge and Whittenton Fail

## Slide 22
City of interest: Taunton
Time elapsed from failure to Peak depth at Taunton: 20 minutes
Peak depth of flood: 6.9 feet - flood elevation exceeded for ~ 12-18 hours
Notes: Schematic showing dam and flood wave through Taunton. Important depth/timing information provided in the text box.

## Slide 23: As for the eventual outcome… A near-failure as the USACE was successful in an emergency operation to draw down the pool and gracefully take down the dam!
In just a matter of hours – note the bowing of the wooden structure!

## Slide 24: USACE to the rescue – While NWS watched Hurricane Wilma like a Hawk They need 84 hours to pull this off – Hurricane Wilma brought rains as forecast ~ hour 96!
During The Flooding
The New Dam

## Slide 25: NWS Response
WFO Taunton was notified 3 pm October 17th – Flash Flood Warning was issued for imminent failure
  Upon issuance, the city of Taunton ordered evacuations of all downstream areas in the floodplain
  Shut down businesses, schools, city offices
RFC/WFO teamed to produce dam breach simulations (DamCrest) program
WFO/RFC provided both remote and on-site Decision Support to the city of Taunton through the following weekend

## Slide 26: A Review of the Whittenton Dam Crisis
Nicole M. Belk
Senior Service Hydrologist
NWS Weather Forecast Office, Taunton, MA
David R. Vallee
Hydrologist-in-Charge
NWS Northeast River Forecast Center, Taunton, MA