## Slide 1: Examining Rainfall forecast uncertainty and its impact on river forecasts
David R. Vallee Hydrologist-in-Charge
NOAA/NWS/Northeast River Forecast Center
Eastern Region Flash Flood Conference

## Slide 2: Objectives
Rainfall forecasting for Rivers – Purpose and expectations
Uncertainty – its origins and meaning
A few examples
New/experimental approach to address the uncertainty as it relates to the river forecasting process
Fishing Creek, Fernville, PA, June 28, 2006
Picture courtesy of http://news.webshots.com

## Slide 3: Rainfall Forecasting - Purpose
Quantitative Precipitation Forecast which is:
  A 24-48 hour forecast representing the expected basin average rainfall in any particular area in discrete 6 hour time steps
  Produced through forecaster analysis of the atmosphere, Numerical Model guidance interpretation, and Hydromet Prediction Center (HPC) forecasts
  It is a key driver/forcing for our river forecasts
  Routine verification conducted

## Slide 4: Rainfall Forecasting - Goal
  Produce the most accurate QPF to provide the most accurate river forecast
  But issues include:
    Nature doesn’t operate on our nice and neat 6 hour time steps
    By its nature – the art/science of rainfall forecasting remains one of our greatest challenges
    By its nature – it is often the greatest source of both river forecast error and uncertainty
At Woonsocket, RI on the Blackstone River a 20 mile displacement on the axis of 4 inch rains = a 4 foot “Over-forecast”!

## Slide 5: Uncertainty - Its origins and meaning
Arises from different places
  Forecaster expertise & experience
  Errors in observations
  Meteorologic and Hydrologic Modeling Systems
    Various resolutions, modeling schemes, antecedent conditions
  Basic nature of the weather system
    Nor’easters & Tropical Cyclones vs. Convection
    The way the rain falls over a basin
  What we are trying to accomplish:
    Nail the rainfall over the right basin, at the right time step, at the right intensity out to 48 hours!!
    The devil is in the almighty details!

## Slide 6: Just how uncertain?
Nature provided a small scale example of this over central New York; May 13-14, 2010
Illustrates several key points;
  No one model will always have the correct answer
  Convective based systems are often the least predictable “until the system ignites”
For Decision Support – our goal is to give you our best forecast but convey the uncertainty and reasons for it; to couch expectations
  Resist the urge to focus on every tenth of a foot in our stage forecasts at longer lead times!

## Slide 7: The Potential Event

## Slide 8: The Potential Event

## Slide 9: So where is the axis of 0.1-2.0 inch rains going to fall?
Global Forecast System (GFS)
North American Model (NAM)
Rainfall Forecast for 6 hour period ending 2 am Fri, May 14th

## Slide 10: So where is the axis of 1-2 inch rains going to fall?
European Forecast Model (ECMWF)
Canadian Forecast Model (GEM)
Rainfall Forecast for 6 hour period ending 2 am Fri, May 14th

## Slide 11: So where is the axis of 1-2 inch rains going to fall?
Observed rainfall ending 2 am 5/14
Northeast River Forecast Center Forecast
Rainfall Forecast for 6 hour period ending 2 am Fri, May 14th

## Slide 12: Lets take a far more significant event June 22-30, 2006 Heavy Rains and Flooding
National Center’s 5 day rainfall forecast
But the devilish details:
  Narrow axis of intense rains positioned east of earlier forecasts
Overforecast of rainfall to the west
Communicating this is a challenge!
Excellent extended lead time to heavy rainfall potential: 4-7 inches forecast
Highly predictable pattern and flood potential was recognized days in advance

## Slide 13: A Different Approach; NCEP s Confidence Forecasts
6 hour forecast – period ending 2 am Fri, May 14
Method objectively quantifies the level of confidence in a given HPC forecast
In general, the larger the spread the greater the uncertainty and thus the lower the confidence
RFCs along the Mississippi are producing river forecasts with each of these forecasts
http://www.hpc.ncep.noaa.gov/qpfci/qpfci.shtml

## Slide 14: A new experimental approach Met-member based ensemble forecasts
Method developed by the Ohio, Mid-Atlantic and Northeast RFCs
Suite of hydrologic forecasts are produced using the Rainfall and Temperature forecasts from two numerical prediction systems

## Slide 15: Uses similar approach to the 30-90 day Ensemble Streamflow Prediction Technique
The Difference:
  These experimental streamflow and melt scenarios are driven by unbiased model forecasts of rainfall and temperature

## Slide 16: Rainfall uncertainty and its impact on River Forecasts

## Slide 17: Don’t forget snowmelt contributions!

## Slide 18: Our Ultimate Goal:

## Slide 19: Examining QPF uncertainty and its impact on river forecasts Questions?
David R. Vallee Hydrologist-in-Charge
NOAA/NWS/Northeast River Forecast Center
Eastern Region Flash Flood Conference